On the GPIO bus, you will need to use the I2C.1 pins plus 3.3v power and ground.  Note, you need a single pull up resistor of 83K or higher between the SCL and 3.3v and another one between SDA 3.3v.  Here is the pin to cable layout:
- GPIO bus pin 5 is SDC --  yellow wire on dIMU cable
- GPIO bus pin 3 is SDA -- white wire on dIMU cable
- GPIO bus pin 1 is +3.3v  -- red wire on dIMU cable
- GPIO bus pin 9 is ground -- black wire on dIMU cable

Here is a picture of the cable
Here is a picture of the 40 pin connector

And here is the full pinout